## Slide 1
SCARLET
SANS data reduction with a reproducible Python workflow
Project presentation and Jupyter Notebook workflow
NeXus / HDF5 native
API Python
Jupyter Notebook
From raw data to I(Q) curves
Raw instrument files
Workflow SCARLET
Reduced I(Q)
v0.2.4

## Slide 2
02
Why SCARLET?
A practical framework for SANS reduction across instruments
A common data language
NeXus/HDF5 is the exchange format from conversion to reduced outputs.
Traceable workflow
Runs, configurations, references, masks, and processing choices are collected in one WorkflowContext.
Notebook for the scientist
The tutorial makes every decision visible while the pipeline applies calculations consistently.
Design principle
Keep the experimental context close to the data, then make reduction steps explicit and repeatable.
Raw files
Context + references
Reduction pipeline
I(Q) + provenance
SCARLET | SANS data reduction
2

## Slide 3
03
Project structure
A small number of modules with clear responsibilities
io/
Readers and converters D11, SANS-LLB, SAM NeXus access
workflow/
WorkflowContext Run tables and configuration Reduction pipelines
reduction/
Physical operations Corrections, geometry Integration and stitching
schemas/
NeXus profiles Validation rules Portable data contracts
User entry points
scarlet convert
scarlet validate
scarlet notebook
scarlet viewer
The notebook is the main interactive route for reduction; the CLI and viewer complement it.
SCARLET | SANS data reduction
3

## Slide 4
04
WorkflowContext is the control centre
It joins experimental metadata, files, and reduction choices
WorkflowContext
single source of workflow state
Runs
sample, water, dark empty cell, beam
Configurations
distance, wavelength beam centre, ROI
References
transmission source flatfield source
Artifacts
masks, NeXus outputs I(Q) text files
Saving and reloading workflow.nxs makes it possible to resume a reduction session.
SCARLET | SANS data reduction
4

## Slide 5
05
Notebook 1: initialise the experiment
Start from the raw directory and generate a structured workflow
from scarlet.workflow.context import \ initialize_workflow_context_from_raw_directory w = initialize_workflow_context_from_raw_directory( RAW_DIR, instrument_name='sansllb', transmission_strategy='opaque_beamstop', output_dir=OUTPUT_DIR, overwrite=True, )
1
Read raw files
Discover the measurement files in RAW_DIR.
2
Convert when needed
Use the instrument converter and write SCARLET NeXus files.
3
Infer the experimental context
Collect runs, configurations, and initial transmission ROIs.
4
Create the output directory
Keep generated data and workflow artifacts together.
Notebook principle: parameters stay visible in the cell and can be reviewed with the analysis.
SCARLET | SANS data reduction
5

## Slide 6
06
Notebook 2: curate the run table
The user validates the experimental meaning before calculations begin
w.write_runs_table_csv('runs_table.csv', overwrite=True) # Edit a copy, then load it back w.update_from_runs_table_csv('runs_filtered.csv') w.runs_table() w.configurations_table() w.save('workflow.nxs', overwrite=True)
What the table contains
entity
sample, water, empty_cell, dark, empty_beam
mode
scattering or transmission
sample name
sample identifier used by the pipeline
configuration
instrument setup used for the measurement
thickness
thickness normalisation when available
This review prevents a technically valid reduction from using the wrong reference or configuration.
SCARLET | SANS data reduction
6

## Slide 7
07
Notebook 3: compute and reuse transmission
Transmission is evaluated per sample and configuration from a detector ROI
w.compute_transmissions() w.write_runs_table_csv('runs_with_transmission.csv', overwrite=True) # Reuse a compatible measurement w.set_transmission_source( config_id='config_2', source_config_id='config_4', )
Transmission logic
1
ROI
Use the central detector region defined for the configuration.
2
Compute
Store the transmission alongside the corresponding run.
3
Declare the source
Explicitly share a compatible transmission between configurations.
The source relationship is declared, not hidden in notebook variables.
SCARLET | SANS data reduction
7

## Slide 8
08
Notebook 4: masks and water normalisation
Prepare the detector corrections that will be consumed by the pipeline
Masks
Masks are edited in the SCARLET viewer, saved with the output data, then attached to the workflow.
w.attach_mask_bundles_from_output_dir() # or: w.set_mask_file(config_id=..., # file_path=...)
They exclude detector regions before integration.
Water flatfield
A water run builds a flatfield for a configuration. A compatible configuration can be explicitly reused.
w.build_water_flatfield(config_id='config_10') w.set_flatfield_source( config_id='config_9', source_config_id='config_10', )
The pipeline then applies flatfield and solid-angle corrections.
SCARLET | SANS data reduction
8

## Slide 9
09
Notebook 5: run the reduction pipeline
One call executes a named sequence of physical processing steps
1
Load
Monitor and dead-time corrections
2
Subtract
Dark and empty-cell references
3
Normalise
Water flatfield and solid angle
4
Scale
Sample thickness when available
5
Integrate
Azimuthal average into I(Q)
6
Write
Processed NeXus and text outputs
pipeline = ReductionPipeline.default() state = pipeline.run_for_sample( workflow=w, sample_name='ludox_SM30', config_id='config_9' ) # Or process all sample scattering runs pipeline.run_all(w)
SCARLET | SANS data reduction
9

## Slide 10
10
What comes out of the notebook?
Reduced data remain inspectable and carry their treatment history
Processed NeXus file
The source file receives a /processed NXentry containing:
• reduced detector data
• uncertainties and coordinates
• masks
• sample and configuration metadata
• named reduction steps and notes
I(Q) text outputs
Each detector can produce a text curve with:
• Q
• I(Q)
• intensity uncertainty
• Q uncertainty when available
• sample, configuration, and transmission provenance
State for inspection
The returned ReductionState gives the notebook immediate access to:
• detectors after each step
• transmission used
• list of applied steps
• warnings and notes
• source file path
SCARLET | SANS data reduction
10

## Slide 11
11
Notebook 6: stitch configurations
Combine reduced I(Q) segments after each configuration has been reduced
from scarlet.workflow.pipeline import StichingPipeline stitch = StichingPipeline(w) stitch.run_all(scale_on='config_10', normalization_factor=1.0)
Stitching logic
1
Load segments
Read the reduced I(Q) curves from processed NeXus entries.
2
Compare overlaps
Estimate relative scale factors in common Q ranges.
3
Select ranges
Keep the useful Q range from each configuration.
4
Apply final scale
normalization_factor multiplies I and I_error, not Q or q_error.
Precondition
Run ReductionPipeline for every scattering configuration before stitching.
SCARLET | SANS data reduction
11

## Slide 12
12
Stitching: from curves to candidate segments
Each configuration + detector pair is treated as an independent segment
A segment contains
• Q and I(Q)
• dI uncertainty
• dQ resolution
• configuration identifier
• detector identifier
Example: c10d2 = config_10 + detector2
A segment is evaluated by its intrinsic quality:
quality = median[(dI / I)² + λres (dQ / Q)²]
Low relative uncertainty and good resolution give a lower score, making a segment preferable.
Illustration on the Q axis
c9d0
c10d0
c10d2
overlap
low Q
high Q
SCARLET | SANS data reduction
12

## Slide 13
13
Stitching: fit two segments in their overlap
The required connection is multiplicative, not a deformation of the curve
1. Build a common Q grid
Both curves are interpolated in their overlap on a common logarithmic grid. The point count is conservative: min(NA, NB).
2. Compute the log-ratio
r(Q) = ln IA(Q) − ln IB(Q)
If the connection is valid, r(Q) forms a plateau.
3. Fit a weighted constant
ln s = sum(wi ri) / sum(wi) with wi = 1 / σri²
σr² = (dIA / IA)² + (dIB / IB)²
The factor s maps segment B onto the scale of segment A: IA(Q) ≈ s IB(Q).
s = exp(ln s)
SCARLET | SANS data reduction
13

## Slide 14
14
Stitching: choose a reliable fitting window
The full overlap is not necessarily the best fitting region
The algorithm tests several windows in the overlap and minimises a quality score.
Reduced χ²
The log-ratio is compatible with a constant.
χ²ν < 3.0
Residual slope
A drift in r(Q) reveals a poor plateau.
|b / σb| < 2.5
Window width
Avoid an artificial agreement over too few points.
at least 8 points Δln Q ≥ 0.10
Resolution
Prefer a lower combined relative resolution.
secondary weighting
A transition is accepted only if the plateau is reliable and the new segment extends Q coverage sufficiently.
SCARLET | SANS data reduction
14

## Slide 15
15
Stitching: select, scale, concatenate
The final chain favours useful segments rather than every available segment
1
Start at low Q
The pipeline starts with the segment having the lowest Qmin.
2
Evaluate candidates
A candidate must connect, have good quality, and extend Qmax.
3
Choose the lowest cost
cost = connection score + segment quality − Q coverage gain.
4
Repeat to the end
Redundant segments or segments without a valid transition are rejected.
Building the final curve
Global factors
GB = GA × sB→A
I and dI are multiplied; dQ is unchanged.
Overlap
A central fraction of the fit is kept for a controlled transition (25% by default).
Reference scale
scale_on sets the reference configuration to a global factor of 1.
SCARLET | SANS data reduction
15

## Slide 16
16
Key message
The notebook is a guided, auditable route from experimental files to reduced curves
SCARLET combines experimental context, explicit correction choices, and reproducible outputs.
1
Start with the run table
Validate samples, references, and configurations before reduction.
2
Use notebook cells as checkpoints
Transmission, masks, and flatfields are visible and reviewable.
3
Run a standard pipeline
Named steps reduce every sample consistently and save provenance.
4
Inspect, then stitch
Work from reduced I(Q) curves and retain physical scale choices.
Project documentation: hibouchen.github.io/scarlet
SCARLET | SANS data reduction
16